## Slide 1
Identifying and evaluating the most attractive pathways for CO2 and CO utilisation for Europe’s Process Industry
Dennis Krämer, DECHEMA e.V.

## Slide 2
Notes: What matters most to you?
We all benefit from the product made by the chemical industry:
Sport shoes, components for cars, petrochemicals get us moving and flying…
Packaging: fresh foods
Isolation material, low energy houses
Health! Medicine etc.

## Slide 3: Feedstock of the organic chemistry
Carbon source for the process industry
…at the roots of most value chains
e.g. plastics in Europe:
46,4 Mio. t
Notes: And the beautiful chemical- well process industries make all the import products that make our life in many cases more easy.
Inhalt:
Plastik in Europa: Packaging, building and construction, automotive, E&E, Others  total 46,4 Mio. t (2010)
20 Mil. T used in the chemical sector (VCI)

## Slide 4: Fossil carbon sources
Notes: As we all know, the conventional carbon source are fossil ones – oil, gas, coal!

## Slide 5
…the whole industry cannot be electrified, yet.
Notes: You may say there are other options to decarbonize the industry
Such as sector coupling – using renewable electricity etc.
However, there are some areas where electrified solotions are not at the horizion: Airplanes, cargo ships

## Slide 6
Evaluation of the potential use of CO2/CO and non-conventional fossil natural resources as feedstock for the process industry in Europe
HORIZON 2020 SPIRE Project
Coordination and Support Action
2016 – 2018
Notes: DECHEMA is a non-profit organisation for chemical engineering and biotechnology. DECHEMA’s goal is to promotes theme-based exchange in a large interdisciplinary network, identify trends in research and technology as well as to shapes progress in chemical engineering, biotechnology and related research fields
Trinomics is an international consultancy that provides research and advice in the fields of energy, environment and climate change
The UK Centre for Carbon Dioxide Utilisation or CDUUK, brings together seven academic departments at the University of Sheffield to focus on the utilization of carbon dioxide as a feedstock for chemical synthesis.

## Slide 7: Introduction - CarbonNext
Carbon sources
Value chains
Products and processes
Industrial symbiosis
Capture and conditioning
Most relevant products and processes
Business model and economics
Economic potential and environmental impact
Carbon efficiency and LCA
Framework conditions
Acceptance and awareness
Price and availability
Game changers
Best practice examples

## Slide 8: WP1: Mapping
“Unconventional” carbon sources?
CO2
CO
Shale gas
Heavy oil
Oil shale
Light tight oil
Tight gas
…

## Slide 9: Limited potential
World shale gas & tight oil resources. Source: WEC (2016)
Only 13 proven crude oil reserves in Europe compared to 226 in the US
Unconventional hydrocarbon resources in Europe are limited
Poor drilling results
Environmental concerns are very high
Conclusion: Moratorium in many EU countries
Notes: Unconventional hydrocarbon resources in Europe are limited. For example, there are only 13 proven crude oil reserves in Europe compared to 226 in the US. Similarly, heavy oil reserves in Europe (0.2 billion barrels of oil in Italy) are a small fraction of the total reserves in the World (59.1 billion barrels of oil). We have identified several production challenges including significant capital investment, environmental issues such as those related to fracking, risk of gas explosions, large water demands and water contamination for CBM’s as well as a need for stable conditions in terms of pressure and temperature which requires a large amount of resources.
We conclude that the potential in Europe is very low and the environmental concerns are very high. We therefore do not foresee that these sources will have an impact on Europe’s processing industry and we propose to disregard them from further research.

## Slide 10: Motivation to use carbon dioxide in the process industry
Climate protection
Reduce CO2 emissions
C source for the process industry
At the roots of most value chains
Energy transition
CO2 as link for sector coupling
PtX for chemical energy storage
One piece of a puzzle
Replace fossil carbon
Broaden the raw material base
Notes: It is expected that the main change in CO2 availability will arise from reductions in emissions arising from coal power generation, which is expected to decrease significantly by 2100. Over the medium term, “clean coal” technologies such as integrated gasification combined cycle or pressurized fluidized bed will improve combustion efficiencies and in the longer term there is expected to be a move away from coal altogether. The relatively ambitious IEA 2°C scenario of the ETP2015 model foresees a reduction of coal as fuel input for electricity and heat generation from 33.8 EJ (1018 J) in 2012 to 5.1 EJ in 2050, corresponding to a 85% reduction. With around 46 % of the global emissions arising from fossil fuel combustion currently coming from coal reductions in coal use will impact CO2 availability. However, the impact upon CO2 utilisation may be limited, as CO2 from this source is generally of low concentration at 12-14% and can be contaminated with sulphur and heavy metals such as mercury, making capture and purification (clean-up) more expensive. Consequently, it is expected that CO2 arising from purer sources will be preferentially utilised as described previously Energy Technology Perspectives 2015, IEA
Trends in global CO2 emissions: (2016) PBL Netherlands Environmental Assessment Agency and EC Joint Research Centre.
Chapter 2 Sources of CO2. IPPC Special Report on Carbon Capture and Storage. https://www.ipcc.ch/pdf/special-reports/srccs/srccs_wholereport.pdf

## Slide 11: Map of key sources of CO2 in Europe (Adapted from E-PRTR)
e-EPTR (European Emission Pollutant and Transfer Register) by the European Environment Agency
  The current E-PRTR lists facilities with CO2 emissions above 0.1 Mt per year
  CO emissions higher than 0.005 Mt have to be reported in the E-PRTR.
  The register contains data reported annually by more than 30,000 industrial facilities within 9 industrial sectors, covering 65 economic activities across Europe.
2000 point source emitters of CO2 in Europe
Total emissions of CO2 in Europe from these facilities amounted to 1,779 Mt in 2014.
Notes: It is expected that the main change in CO2 availability will arise from reductions in emissions arising from coal power generation, which is expected to decrease significantly by 2100. Over the medium term, “clean coal” technologies such as integrated gasification combined cycle or pressurized fluidized bed will improve combustion efficiencies and in the longer term there is expected to be a move away from coal altogether. The relatively ambitious IEA 2°C scenario of the ETP2015 model foresees a reduction of coal as fuel input for electricity and heat generation from 33.8 EJ (1018 J) in 2012 to 5.1 EJ in 2050, corresponding to a 85% reduction. With around 46 % of the global emissions arising from fossil fuel combustion currently coming from coal reductions in coal use will impact CO2 availability. However, the impact upon CO2 utilisation may be limited, as CO2 from this source is generally of low concentration at 12-14% and can be contaminated with sulphur and heavy metals such as mercury, making capture and purification (clean-up) more expensive. Consequently, it is expected that CO2 arising from purer sources will be preferentially utilised as described previously Energy Technology Perspectives 2015, IEA
Trends in global CO2 emissions: (2016) PBL Netherlands Environmental Assessment Agency and EC Joint Research Centre.
Chapter 2 Sources of CO2. IPPC Special Report on Carbon Capture and Storage. https://www.ipcc.ch/pdf/special-reports/srccs/srccs_wholereport.pdf

## Slide 12: Preliminary conclusions on CO2 sources
There are plentiful sources of CO2 which could be used as a carbon feedstock for the process industry in Europe.
The most prevalent emitter of CO2 are power plants. Due to the lower CO2 concentration in the emissions from the power sector most of the largest emitters are not included in the primary target sources.
First target: Sources with the highest concentration of CO2 such as:
Hydrogen production
Natural gas processing
Ethylene oxide manufacture
Ammonia production
Notes: There are plentiful sources of CO2 which could be used as a carbon feedstock for the process industry in Europe. Primary targets for sourcing CO2 should focus on those sources with the highest concentration of CO2, (Hydrogen production, natural gas processing, ethylene oxide manufacture and ammonia production) as the higher concentration of CO2 reduces the cost of capture. However, larger volumes of CO2 are available from the iron and steel industry and cement industries, albeit at lower CO2 concentration. As industries look to decarbonise (particularly the iron and steel and cement sectors) there is an observed market pull to deploy CO2 utilisation technologies to provide an economically beneficial method of reducing CO2 emissions. As next-generation carbon capture technologies reach the market, other sources of CO2 may become increasingly economically viable.
It is expected that the main change in CO2 availability will arise from reductions in emissions arising from coal power generation, which is expected to decrease significantly by 2100. Over the medium term, “clean coal” technologies such as integrated gasification combined cycle or pressurized fluidized bed will improve combustion efficiencies and in the longer term there is expected to be a move away from coal altogether. The relatively ambitious IEA 2°C scenario of the ETP2015 model foresees a reduction of coal as fuel input for electricity and heat generation from 33.8 EJ (1018 J) in 2012 to 5.1 EJ in 2050, corresponding to a 85% reduction. With around 46 % of the global emissions arising from fossil fuel combustion currently coming from coal reductions in coal use will impact CO2 availability. However, the impact upon CO2 utilisation may be limited, as CO2 from this source is generally of low concentration at 12-14% and can be contaminated with sulphur and heavy metals such as mercury, making capture and purification (clean-up) more expensive. Consequently, it is expected that CO2 arising from purer sources will be preferentially utilised as described previously Energy Technology Perspectives 2015, IEA
Trends in global CO2 emissions: (2016) PBL Netherlands Environmental Assessment Agency and EC Joint Research Centre.
Chapter 2 Sources of CO2. IPPC Special Report on Carbon Capture and Storage. https://www.ipcc.ch/pdf/special-reports/srccs/srccs_wholereport.pdf

## Slide 13: CO emissions and chemical parks
Total CO emissions in the EU: 3.38 Mt
Metal sector is the primary CO emitter in the EU: 2.4 Mt
Chart: CO emissions 2014
| Chemical | Construction | Energy | Food/Agriculture | Metal | Mining | Other | Paper | Waste
Mtonnes | 0.32585 | 0.36446 | 0.20053 | 0.017598 | 2.4175 | 0.000598 | 0.003955 | 0.03528 | 0.019643
Mtonnes % | 0.096269 | 0.10768 | 0.059244 | 0.0051991 | 0.71422 | 0.00017667 | 0.0011685 | 0.010423 | 0.0058033

## Slide 14: CO emitted by sectors
Chart: Metal sector
| Treatment and coating of metals | Manufacture of other non-metallic mineral products n.e.c. | Other non-ferrous metal production | Manufacture of basic iron and steel and of ferro-alloys | Lead, zinc and tin production | Forging, pressing, stamping and roll-forming of metal; powder metallurgy | Copper production | Casting of steel | Casting of iron | Casting of light metals | Casting of other non-ferrous metals | Aluminium production
Mtonnes % | 0.053237 | 1.2939 | 0.23826 | 92.1571 | 0.062503 | 0.02213 | 0.12927 | 0.088108 | 0.82751 | 0.096381 | 0.046329 | 5.0066
Chart: Chemicals
| Manufacture of refractory products | Manufacture of refined petroleum products | Manufacture of plastics in primary forms | Manufacture of other organic basic chemicals | Manufacture of other inorganic basic chemicals | Manufacture of other chemical products n.e.c. | Manufacture of oils and fats | Manufacture of fertilisers and nitrogen compounds | Manufacture of dyes and pigments | Manufacture of coke oven products
Mtonnes % | 0.6506 | 15.6868 | 1.0815 | 7.6501 | 64.3161 | 1.4424 | 0.23109 | 0.99769 | 2.9124 | 4.2556
Chart: Construction
| Manufacture of bricks, tiles and construction products, in baked clay | Manufacture of cement | Manufacture of lime and plaster | Manufacture of veneer sheets and wood-based panels
Mtonnes % | 1.3708 | 69.9759 | 26.0177 | 2.6357
Chart: Energy
| Transport via pipeline | Steam and air conditioning supply | Production of electricity | Manufacture of gas
Mtonnes % | 0.77644 | 1.7294 | 97.186 | 0.30818
Manufacture of iron and steel productes 65% of total CO emissions
Focus on steel industry as main emitter

## Slide 15: Main conclusions on CO
Steel industry is the main CO emitter
  Only minor part is emitted and appears at the E-PRTR database
  Most of the is CO used for heating or electrification
  Alternative cross-sectional use is limited at the moment
    political framework conditions (e.g. German renewable energy act, EEG) and infrastructure for transportation
    Chemical/physical processes known, technical feasibility on industrial scale is missing
CO estimation
  Rough estimation possible
  Increase in factor 12-20 for single sources
Notes: CO can be an alternative C-source if …
  significant amounts available (point sources such as SiC factory in Spain)
  Consumer close-by, infrastructure easily to install
  political framework conditions support alternative usage pathways
  technical feasibility of techniques for cleaning, separation and conditioning were shown
Steel industry as point sources
Only CO emitted into the atmosphere is listed
  Does not reflect the CO produced as most CO is directly reused on site
  Facilities are known
Amount of CO produced could be calculated
  Requires detailed information on steel industry and plant facts
  Estimation based on single cases (e.g. Duisburg, Germany) prepared
  Rough estimation for EU

## Slide 16
*All images by Fotolia